The price/performance standard in side-address studio condenser microphone technology Ideal for project/home-studio applications High SPL handling and wide dynamic range provide unmatched versatility Custom-engineered low-mass diaphragm provides extended frequency response and superior transient response Cardioid polar pattern reduces pickup of sounds from the sides and rear, improving isolation of desired sound source Pivoting, threaded stand mount attaches securely for easy and precise placement of the microphone

AT2020 Specifications Element Signal to Noise Ratio Condenser 74 dB, 1 kHz at 1 Pa Polar Pattern Dynamic Range (Typical) Cardioid 124 dB, 1 kHz at Max. SPL Frequency Response Phantom Power Requirements 20 - 20,000 Hz 48V DC, 2 mA typical Open Circuit Sensitivity Noise -37 dB (14.1 mV) re 1V at 1 Pa 20 dB SPL Impedance Weight 100 ohms 12.1 oz (345 g) Maximum Input Sound Level Output Connector 144 dB SPL, 1 kHz at 1% T.H.D. Integral 3-pin XLRM-type

Accessories Furnished: Stand mount; 5/8"-27 to 3/8"-16 threaded adapter; protective pouch