Guitar/Bass

## Live Sound

- Smallest switchable transmitter

- Up to 11 hours battery time with one AAA size Battery

- Frequency response optimized for guitar and bass

- Patented Flexx-Jack matching all guitar outputs

- Three different battery covers fitting perfectly to your guitar

# Text boxes

GB 40 Flexx works only with one AAA battery and has more than 11 hours lifetime - this is the lowest operating cost in this class. The frequency response is optimized for guitar and bass - it can be used for keyboards and all instruments with a jack plug, too. The patented FlexxJack-Plug is matching all guitar outputs with an included long adapter jack.

The GB 40 guitarbug is probably the easiest way to turn a guitar, bass, or portable keyboard into a wireless instrument. The FlexJack swivel jack plug will mate with any type of output jack and is spring loaded to hold the GB 40 securely against the instrument. In addition, the GB 40 is so small that it is almost invisible and won't be in your way while playing. Since the GB 40 sits right on top of the instrument's output jack, the noiseless on/mute/off switch and gain control are always within easy reach.

The GB 40 Flexx will be available as single version and as “guitar set” version with a stationary receiver SR 40 Flexx.

GB 40 FLEXX

Specifications

Carrier frequency range 	660 to 865 MHz

Modulation 			FM

Frequency stability 		(-10°C to +50°C) ±15 kHz

RF output 			typ. 5 mW

Compander			integrated

Audio bandwidth 		40 to 20,000 Hz

Audio input impedance 	1 Mohm

Max. audio input level 	1100 mV/1 kHz

T.H.D. at 1 kHz 		typ. 0.8%

Signal/noise ratio 		typ. 103 dB(A)

Power requirement 		single 1.5-V AAA size battery

Current consumption 		typ. 75 mA

Battery life 			>11/>6 hours (dry/rechargeable battery)

Size 				(WxDxH) 76 x 20 x 28 mm (3 x 0.8 x 1.1 in.)

##### Net weight 			28 g (1 oz.)

Order Number:

7617 H XXXXX GB Flexx Single

3109 H XXXXX GB Flexx Guitar Set (SR 40 Pro Flexx, GB Flexx)